## Slide 1
Furtively Connecting IoT Devices
with Acoustic Noise
1School of Electronic Information and Electrical Engineering, Shanghai Jiao Tong University
2School of Software and BNRist, Tsinghua University
Meng Jin1, Yuan He2, Yunhao Liu2 , Xinbing Wang1
Notes: Hello everyone. My name is Meng Jin.
I come from Shanghai Jiao Tong university.
Today, I’m going to share with you our recent work on how we can furtively connect IoT devices with noise signal
This is a joint work between shanghai jiao tong university and Tsinghua university.

## Slide 2
IoT devices are prevalent nowadays…
Notes: In recent years, IoT devices are widely used in our home and office.

## Slide 3
IoT devices are prevalent nowadays…
Notes: All of these devices continuously share extensive information, about the users and the environment.

## Slide 4
Potential privacy risks
Private information shared among IoT device
Side channel information from the signal itself
Health condition
Activity
Trade information
Making the communication undetectable
Traffic pattern
Location
Motion
Notes: For example, wearable devices may share user’s health conditions
D2D communication for authentication may leak user’s password
And, besides the data that shared between the IoT devices, the features of the wireless signal itself can also leak private information.
For example, by observing how the user affects the features of the wireless signal, we can infer user’s activity.
So, an urgent problem now is: how to make the communication undetectable by the attacker.

## Slide 5
Large quantity of deployed tags
Existing solutions
A potential solution is to hide the communication with the channel:
Notes: A potential solution is to hide the communication leveraging the wireless channel.
Specifically, suppose the transmitted signal is x. The received signal is x multiplies the channel h
To ensure that the eavesdropper cannot detect the signal x, we can randomize the channel to hide any pattern in the signal.
However, in these methods, we need to ensure that the transmitter’s ability to hide the signal is higher than the eavesdropper’s ability to extract the signal.
Consider that the eavesdropper can use either advanced receiving hardware or advanced signal processing technology.
We can never win the battle using IoT devices.

## Slide 6
Existing solutions
A potential solution is to hide the communication with the channel:
Eavesdropper’s ability to extract the signal
Transmitter’s ability to hide the signal
V.S.
Lose!
Notes: A potential solution is to hide the communication leveraging the channel that the signal propagates through.
Specifically, suppose the transmitted signal is x. The received signal is x multiplies by the channel h
To ensure that the eavesdropper cannot detect the signal x, we can randomize the channel to hide any pattern in the signal.
However, in these methods, we need to ensure that the transmitter’s ability to hide the signal is higher than the eavesdropper’s ability to extract the signal.
Consider that the eavesdropper can use either advanced receiving hardware or advanced signal processing technology.
We can never win the battle using IoT devices.

## Slide 7
Rustle: Random noise communication
Change the hardware game  Randomizing the signal itself
Random noise with hidden pattern that can be seen only by legitimate receiver
0 1 0 0 0 1 0 1 1 0
Acoustic noise
Notes: To change the game, we do not try to hide the signal under randomized channel.
Instead, we directly randomize the signal itself.
Specifically, we design a communication system, which connects IoT devices with acoustic noise. This signal can be easily exchanged between the widely used speakers and microphones on IoT devices.
We embed the information into the hidden pattern of the random signal.
This pattern can be only seen by the legitimate receiver.
While for the eavesdropper, the signal resembles a noise.

## Slide 8
Furtive modulation
What kind of signal pattern is suitable for such furtive communication?
Solution: leveraging the weak transitivity of correlation coefficient
A
B1
Bn
B2
……
High correlation between and
Low correlation between and
Notes: Now the problem is: what kind of signal pattern is suitable for such furtive communication?
Our solution is to leverage the weak transitivity of signal’s correlation.
We find that, for a sequence A, we can find a set of signal B1 to Bn, whose correlation with Sequence A is high,
While the mutual correlation between Sequence Bs can be controlled to be very low.

## Slide 9
Furtive modulation
Embed the information to each noise sequence by adjusting its correlation with a “key” sequence.
……
……
Bit “1”
Bit “0”
Secret Key
Uncorrelated!
Notes: So, we can embed information in a noise sequence by adjusting its correlation with a secret key.
And this secret key is shared by the legitimate transceivers
For example, we can generate a set of signal whose correlation with the secret key is 0.5
And we use these sequences to represent bit 1
We can also generate a set of signal whose correlation is -0.5, and use them to generate bit 0
And note that all those sequences are almost uncorrelated with each other.
Then the transmitter can use these sequence to embed its information like this

## Slide 10
Furtive modulation
1
Embed the information to each noise sequence by adjusting its correlation with a “key” sequence.
Notes: Now, for the legitimate receiver, since he knows the secret key, he can then decode the signal by calculating the correlation between the signal and the secret key.
When the correlation result is larger than 0, a bit 1 is obtained.
Otherwise, a bit zero is obtained.
Then it can obtain all the bits with a moving window.

## Slide 11
Furtive modulation
1
Embed the information to each noise sequence by adjusting its correlation with a “key” sequence.
0
Notes: Now, for the legitimate receiver, since he knows the secret key, he can then decode the signal by calculating the correlation between the signal and the secret key.
When the correlation result is larger than 0, a bit 1 is obtained.
Otherwise, a bit zero is obtained.
Then it can obtain all the bits with a moving window.

## Slide 12
Furtive modulation
1
Embed the information to each noise sequence by adjusting its correlation with a “key” sequence.
0
1
Notes: Now, for the legitimate receiver, since he knows the secret key, he can then decode the signal by calculating the correlation between the signal and the secret key.
When the correlation result is larger than 0, a bit 1 is obtained.
Otherwise, a bit zero is obtained.
Then it can obtain all the bits with a moving window.

## Slide 13
Furtive modulation
1
Embed the information to each noise sequence by adjusting its correlation with a “key” sequence.
0
1
0
Notes: Now, for the legitimate receiver, since he knows the secret key, he can then decode the signal by calculating the correlation between the signal and the secret key.
When the correlation result is larger than 0, a bit 1 is obtained.
Otherwise, a bit zero is obtained.
Then it can obtain all the bits with a moving window.

## Slide 14
Furtive modulation
1
Embed the information to each noise sequence by adjusting its correlation with a “key” sequence.
0
1
0
-0.16
-0.15
-0.17
0.14
0.15
-0.16
Low mutual correlation
Notes: While, for the eavesdropper, since it doesn’t know the secret key.
It can detect the transmission only by calculating the mutual correlation between the sequences.
While, since all the sequence are controlled to have very low mutual correlation.
So the eavesdropper cannot distinguish between the modulated signal and the random noise.

## Slide 15
Furtive modulation
1
Embed the information to each noise sequence by adjusting its correlation with a “key” sequence.
0
1
0
-0.16
-0.15
-0.17
0.14
0.15
-0.16
Low mutual correlation
How we can generate those signals?
Notes: Now, the problem is: how we can generate those signals?

## Slide 16
Furtive modulation
1
Embed the information to each noise sequence by adjusting its correlation with a “key” sequence.
0
1
0
-0.16
-0.15
-0.17
0.14
0.15
-0.16
Low mutual correlation
How we can generate those signals?
How we can find a set of sequences that satisfies:
The correlation between each sequence and the key is controlled at
The mutual correlation between each two sequences and is controlled at
Reliability
Security
Notes: How we can find a set of sequence (x1 to xN), whose correlation to the key sequence is equal to a required value;
And the mutual correlation between each two sequences is low
To answer this question, we first model this problem as a high-dimensional geometric problem

## Slide 17
Modeling the correlation
A point in a
L-dimensional space
A L-length signal sequence
A L-length signal sequence can be in essence modeled as a point (vector) in a L-dimensional space.
Notes: Specifically, for each L-length signal sequence xi, it can be modeled as a point in a L-dimensional space.
For example when the length of the signal sequence is 3.
The signal can be represented as a point in a 3D space

## Slide 18
Modeling the correlation
A 3-length signal sequence
A L-length signal sequence can be in essence modeled as a point (vector) in a L-dimensional space.
A point in a
L-dimensional space
Notes: Specifically, for each L-length signal sequence xi, it can be modeled as a point in a L-dimensional space.
For example when the length of the signal sequence is 3.
The signal can be represented as a point in a 3D space

## Slide 19
Modeling the correlation
A point in a
3-dimensional space
A 3-length signal sequence
A L-length signal sequence can be in essence modeled as a point (vector) in a L-dimensional space.
Notes: Specifically, for each L-length signal sequence xi, it can be modeled as a point in a L-dimensional space.
For example when the length of the signal sequence is 3.
The signal can be represented as a point in a 3D space

## Slide 20
Modeling the correlation
The correlation between two sequences and is defined as the cosine of the angle between the corresponding two vectors.
Notes: Now, if we have two sequence, the correlation between them is represented by the angle between the two vectors.
Recall that we requires the correlation between the key and each sequence xi is controlled at a certain value, so all the signal vectors have to diverge from the key with the same angle \theta, forming a conical surface.
Recall that we also require that the mutual correlation between each two sequences is lower than a certain value.
We should select a set of vectors on the surface, making their pairwise angles \theta_ij larger than a predefined value \theta_mu.
By projecting vectors x on this 2D space as x′, the above problem can be transformed to the problem of finding a set of vectors X′ on this circle where the angle between any two vectors is larger than a certain angle θmu’.
The relationship between θmu and θmu’ is given by this equation.

## Slide 21
Modeling the correlation
The correlation between two sequences and is defined as the cosine of the angle between the corresponding two vectors.
Notes: Now, if we have two sequence, the correlation between them is represented by the angle between the two vectors.
Recall that we requires the correlation between the key and each sequence xi is controlled at a certain value, so all the signal vectors have to diverge from the key with the same angle \theta, forming a conical surface.
Recall that we also require that the mutual correlation between each two sequences is lower than a certain value.
We should select a set of vectors on the surface, making their pairwise angles \theta_ij larger than a predefined value \theta_mu.
By projecting vectors x on this 2D space as x′, the above problem can be transformed to the problem of finding a set of vectors X′ on this circle where the angle between any two vectors is larger than a certain angle θmu’.
The relationship between θmu and θmu’ is given by this equation.

## Slide 22
Modeling the correlation
The correlation between two sequences and is defined as the cosine of the angle between the corresponding two vectors.
Notes: Now, if we have two sequence, the correlation between them is represented by the angle between the two vectors.
Recall that we requires the correlation between the key and each sequence xi is controlled at a certain value, so all the signal vectors have to diverge from the key with the same angle \theta, forming a conical surface.
Recall that we also require that the mutual correlation between each two sequences is lower than a certain value.
We should select a set of vectors on the surface, making their pairwise angles \theta_ij larger than a predefined value \theta_mu.
By projecting vectors x on this 2D space as x′, the above problem can be transformed to the problem of finding a set of vectors X′ on this circle where the angle between any two vectors is larger than a certain angle θmu’.
The relationship between θmu and θmu’ is given by this equation.

## Slide 23
Modeling the correlation
The correlation between two sequences and is defined as the cosine of the angle between the corresponding two vectors.
Notes: Now, if we have two sequence, the correlation between them is represented by the angle between the two vectors.
Recall that we requires the correlation between the key and each sequence xi is controlled at a certain value, so all the signal vectors have to diverge from the key with the same angle \theta, forming a conical surface.
Recall that we also require that the mutual correlation between each two sequences is lower than a certain value.
We should select a set of vectors on the surface, making their pairwise angles \theta_ij larger than a predefined value \theta_mu.
By projecting vectors x on this 2D space as x′, the above problem can be transformed to the problem of finding a set of vectors X′ on this circle where the angle between any two vectors is larger than a certain angle θmu’.
The relationship between θmu and θmu’ is given by this equation.

## Slide 24
3D code
Spherical code problem
Furtive modulation of L-length sequences can be modeled as a ()-dimensional spherical code problem.
2D code
Notes: When extended to a L-dimensional space, the modulation problem can be modeled as a spherical code problem.
That is finding a set of vectors X′ on a (L-1)-dimensional hypersphere, where the angle between any two vectors xi and xj is larger than a pre-defined value thetaij.
This two figures shows the cases of 2d and 3D spherical code problem.

## Slide 25
Signal Generation
Finding spherical codes in a ()-dimensional space where the minimal pairwise angle of the vectors is maximized
2D Space
3D Space
(L-1)-D Space
Start with a random
set of vectors
Iteratively splay the vector pairs with small angels
Notes: But how to achieve this in high dimensional space?
We achieve this with a searching algorithm where we start with a set of random vectors.
And we iteratively splay the vectors so that the maximum pairwise angle is minimized.
This animation shows examples of this process in 2D and 3D.

## Slide 26
Signal Generation
Finding spherical codes in a ()-dimensional space where the minimal pairwise angle of the vectors is maximized
3D Space
(L-1)-D Space
Start with a random
set of vectors
Iteratively splay the vector pairs with small angels
2D Space
Notes: But how to achieve this in high dimensional space?
We achieve this with a searching algorithm where we start with a set of random vectors.
And we iteratively splay the vectors so that the maximum pairwise angle is minimized.
This animation shows examples of this process in 2D and 3D.

## Slide 27
Signal Generation
Finding spherical codes in a ()-dimensional space where the minimal pairwise angle of the vectors is maximized
3D Space
(L-1)-D Space
Start with a random
set of vectors
Iteratively splay the vector pairs with small angels
2D Space
Notes: But how to achieve this in high dimensional space?
We achieve this with a searching algorithm where we start with a set of random vectors.
And we iteratively splay the vectors so that the maximum pairwise angle is minimized.
This animation shows examples of this process in 2D and 3D.

## Slide 28
Signal Generation
Finding spherical codes in a ()-dimensional space where the minimal pairwise angle of the vectors is maximized
3D Space
(L-1)-D Space
Start with a random
set of vectors
Iteratively splay the vector pairs with small angels
2D Space
Notes: But how to achieve this in high dimensional space?
We achieve this with a searching algorithm where we start with a set of random vectors.
And we iteratively splay the vectors so that the maximum pairwise angle is minimized.
This animation shows examples of this process in 2D and 3D.

## Slide 29
Signal Generation
Finding spherical codes in a ()-dimensional space where the minimal pairwise angle of the vectors is maximized
3D Space
(L-1)-D Space
Start with a random
set of vectors
Iteratively splay the vector pairs with small angels
2D Space
Notes: But how to achieve this in high dimensional space?
We achieve this with a searching algorithm where we start with a set of random vectors.
And we iteratively splay the vectors so that the maximum pairwise angle is minimized.
This animation shows examples of this process in 2D and 3D.

## Slide 30
Signal Generation
Finding spherical codes in a ()-dimensional space where the minimal pairwise angle of the vectors is maximized
3D Space
(L-1)-D Space
Start with a random
set of vectors
Iteratively splay the vector pairs with small angels
2D Space
Notes: But how to achieve this in high dimensional space?
We achieve this with a searching algorithm where we start with a set of random vectors.
And we iteratively splay the vectors so that the maximum pairwise angle is minimized.
This animation shows examples of this process in 2D and 3D.

## Slide 31
Signal Generation
Finding spherical codes in a ()-dimensional space where the minimal pairwise angle of the vectors is maximized
3D Space
(L-1)-D Space
Start with a random
set of vectors
Iteratively splay the vector pairs with small angels
2D Space
Notes: But how to achieve this in high dimensional space?
We achieve this with a searching algorithm where we start with a set of random vectors.
And we iteratively splay the vectors so that the maximum pairwise angle is minimized.
This animation shows examples of this process in 2D and 3D.

## Slide 32
Signal Generation
Finding spherical codes in a ()-dimensional space where the minimal pairwise angle of the vectors is maximized
3D Space
Notes: Then for each point, we can generate a noise sequence
And then we use these sequences to perform furtive communication between legitimate devices.

## Slide 33
Signal Generation
Finding spherical codes in a ()-dimensional space where the minimal pairwise angle of the vectors is maximized
…
Notes: Then for each point, we can generate a noise sequence
And then we use these sequences to perform furtive communication between legitimate devices.

## Slide 34
Signal Generation
Finding spherical codes in a ()-dimensional space where the minimal pairwise angle of the vectors is maximized
…
Notes: Then for each point, we can generate a noise sequence
And then we use these sequences to perform furtive communication between legitimate devices.

## Slide 35
Evaluation
Implementation & evaluation
Notes: Now, let’s look at the performance.

## Slide 36
Implementation & settings
Receiver
Four different types of smartphones:
SAMSUNG Galaxy S10
SAMSUNG Galaxy S9
Xiaomi note9
Xiaomi Pro10
Arduino Uno board
Sender
Microsoft Surface Laptop 2
JBL PS2200 loudspeaker
Notes: We implement Rustle on different devices, and also test its performance in different environments.

## Slide 37
Implementation & settings
Environment
Resident
Coffee shop
Metrics
The eavesdropper's error rate on detecting the signal
Including both the false alarm rate and miss detection rate
Bit Error Rate
Notes: We implement Rustle on different devices, and also test its performance in different environments.

## Slide 38
Impact of ambient noise
Volume
Frequency
Type
Rustle can simultaneously achieve PE > 80% and BER < 1%
Notes: This three figures show the performance under ambient noises with different volumes, frequencies, and types.
As can be seen, the all the three factor do not have obvious impact on the performance of Rustle.
It can always achieve a lower than 1% BER while the eavesdropper’s error in detecting the communication is higher than 80%.

## Slide 39
Coverage
Legitimate receiver
EVE
Larger distance
NLoS Transmission
Notes: We further conduct an experiment in a practical indoor environment to understand the coverage of our system.
These two figures shows the heat maps of BER and the eavesdropper’s error rate in detecting the communication.
As can be seen, in more than 85% area in the apartment, the eavesdropper’s error rate is higher than 90%，while the coverage for the legitimate transmission is higher than 95%.
Specifically, we deploy one sender in an one-bedroom apartment. We place the receiver on 8 different locations with different distance and direction to the sender.
As can be seen, some locations suffer through-obstacle transmission.
This figure shows the BER obtained when the receiver is placed at different locations. We find that:
Signal’s propagation direction do not have obvious affect on BER when signal’s arriving angle is less than 90 degree
Second, in the case of through-obstacle transmission, Rustle can still achieve decent performance.
And these two figures shows the heat maps of BER and the eavesdropper’s error rate in detecting the communication.
As can be seen, in more than 85% area in the apartment, the eavesdropper’s error rate is higher than 90%， while the coverage for the legitimate transmission is higher than 95%.

## Slide 40
Conclusion
We propose a new form of modulation which embeds information in a series of mutually orthogonal noise sequences.
The proposed system Rustle provides the following benefits:
  Easy to deploy on IoT devices;
  Does not require an advantage in the legitimate channel;
  Parallel transmission.
We design and implement Rustle on commodity hardware and evaluated its performance through extensive experiments.
Notes: In conclusion, we propose a new form of modulation, which embeds information in a series of mutually uncorrelated noise sequences.
The proposed method is reliable and efficient, and more importantly it is easy to deploy on IoT devices.
We implement the system on commodity hardware and evaluated its performance with extensive experiments.

## Slide 41
Thanks
Q&A
Notes: Thank you so much for your attention
I’m happy to take your question