## Slide 1: WiZig: Cross-Technology Energy Communication over a Noisy Channel
Xiuzhen Guo , Xiaolong Zheng , Yuan He
Tsinghua University
INFOCOM 2017
Notes: Good morning everyone, I’m Xiuzhen Guo
Today, I’m going to share with you our recent work titled “wizig: Cross-technology energy communication over a noisy channel”

## Slide 2
Wireless is Everywhere
How to achieve cross-technology communication (CTC)?
Preliminary Study
Design
Evaluation
Notes: The mainstream wireless technology includes WiFi, ZigBee and Bluetooth.
They share the same frequency band and coexist in the same physical space.
So how to deliver data across different technologies remains an open problem.

## Slide 3
Build Indirect Connections
Cloud
Have access to the Internet
Transmission delay
Additional wireless traffic
Transmission delay
Deployment and maintenance cost
GateWay
Preliminary Study
Design
Evaluation
Notes: Early works to address the above problem propose to build indirect connections among these devices.
Cloud is a choice to exchange data among from individual systems. But this method requires that devices have
access to the Internet. Besides, the exchange has considerable transmission delay.
Another way is to connect the coexisting devices through a local gateway. However, the relay will bring significant additional wireless traffic. Besides, the dedicated gateway will increase the deployment and maintenance [‘mentənəns] cost.
In the iron man, Just imagine that if the time delay between the watch and the sensor is great, tony would wake up later and mybe his wife would be hurt.
Timely and efficient data exchange among those devices is very important

## Slide 4
How to achieve direct cross-technology communication(CTC)?
[1] FreeBee: MobiCom’15; [2] Esense: MobiCom’09; [3]Gap Sense: InfoCom’13
Different PHY and MAC standards IEEE 802.11 Vs IEEE 802.15.4
Is there any available information medium?
Time (FreeBee[1]) Vs Frequency Vs Amplitude (Esense[2] GapSense [3])
How to resist channel noise?
Preliminary Study
Design
Evaluation
Notes: Direct cross-technology communication appears to be a more promising ['prɑmɪsɪŋ] direction.
At the same time, this is a also a challenging task.
First, , these technologies follow different standards. For example, Wifi follows the IEEE 802.11 and zigbee follows the ieee 802.15.4. so a device cannot directly decode the standardized ['stændə,daizd] data from another technology.
Second, Is there any available information medium? The existing proposals [prə'pozl] try to exploit free side-channels as information carriers. Regarding the wireless medium, a side channel typically exists in the following three dimensions: time, frequency and amplitude.
FreeBee [17] is a representative ['rɛprɪ'zɛntətɪv] work in the temporal dimension. It enables direct unicast and cross technology broadcast by embedding the data into beacons and shifting their transmission timings. But The achievable date rate of FreeBee is bounded by the beacon rate of commercial WiFi devices.
they operate on the same frequency band. So frequency dimension is not available.
Esense is the first work that uses energy sampling realizing data transmission from WiFi to ZigBee devices. It controls the absence or presence ['prez(ə)ns] of data packets to encode 0/1 bits in the amplitude dimension.
Third, Since the communication channel is intrinsically noisy, it is not a trivial ['trɪvɪəl] to reduce the harmful impact of noise and realize low error rate.

## Slide 5
Energy communication
Energy can be used as a medium of communication
There is enough Energy gap in real environment
Preliminary Study
Design
Evaluation
Notes: To investigate that Energy can be used as a medium of communication, we conduct several experiments.
We control one AP as transmitter and one noise AP to generate jamming. the RRSI sequence is shown as this figure. We can find that packets and noise can be separated['sɛpəretɪd]
clearly because the RSSI gap between packets and noise is large.
In addition, We can find that the RSSI values will decrease when increasing the distance between the AP and node.
We also study the RSSI distribution in various real indoor environments. The RSSI distributions of different places are different. But no matter in which environments, there are enough energy gap and coding space.

## Slide 6
Basic Design of WiZig
Only transmits one bit in one fixed receiving window
Preliminary Study
Design
Evaluation
Notes: Based on the above facts, we propose WiZig, a practical CTC protocol. It achieves the data transmission from WiFi to zigbee by leaveraging the energy as a communication medium.
This is the basic design of WiZig.
Take the two energy levels as an example.
The WiZig sender modulates data as the presence and absence of WiFi packets to represent symbol “1” and “0”. After encoding and modulation, the sender transmits these WiFi packets without modifying the PHY layer.
The receiver detects the RSSI values within a time window T. If the receiver detects a certain number of packet sample points, then it will decode the symbol as “1”. Otherwise, the receiver decodes the symbol as “0”.
It is obvious that the channel resource is not fully exploited if only transmitting one bit in one fixed receiving windows

## Slide 7
Amplitude Modulation of WiZig
Transmits multiple bits in one fixed receiving window
Maximum energy levels:
Preliminary Study
Design
Evaluation
Notes: Next, we propose amplitude modulation that increases the number of energy levels to encode more bits at once for improving data rate.
Without losilng generality[,dʒɛnə'ræləti], we take the modulation of four energy levels as an example.
The WiZig sender transmits packets with three different powers to provide three energy levels that can be encoded as 01, 10, 11. And the absence of packet is encoded as 00. The WiZig receiver samples the RSSI on channel and it can detect four different energy levels. Then the receiver can decode 2 bits data at once.
The number of energy levels can be divided in theory is:N =RSSI/△RSSI, where RSSI is the max signal strength at the receiver and △RSSI is the minimum RSSI gap between two adjacent energy levels.
However, the energy communication channel is noisy and dynamic. Using multiple energy levels can increase the error rate under the noisy channel because noise can corrupt the RSSI pattern of two adjacent energy levels. Hence, it is important to reduce the harmful impact of noise to improve the throughput without increasing the error rate.

## Slide 8
Temporal Modulation of WiZig
Transmits multiple bits in one receiving window with different length
Preliminary Study
Design
Evaluation
Notes: Compared with Amplitude modulation, Temporal modulation is relatively more robust to noise. We propose temporal modulation to be more resilient to the dynamic noise on wireless channel.
WiZig extends the length of receiving window to reduce the error rate when the channel quality is poor and shorten the length of time window to improve the date rate when the channel quality is good.
As four energy levels as an example, The WiZig sender transmits packets and the window length of the receiver will be adjusted according to the channel noise. The stronger the noise is, the larger the window length is.

## Slide 9
Theoretical Analysis
Preliminary Study
Design
Evaluation
 | Two Energy levels | Multiple Energy levels
Bit Error Rate (BER) |  | 
Symbol Error Rate (SER) |  | 
 | Two Energy levels | Multiple Energy levels
Bit Error Rate (BER) |  | 
Symbol Error Rate (SER) |  | 
SNR
The number of energy levels
The length of receiving window
Notes: We model the energy channel and analyze ['ænə,laɪz] the relationship BER, SER ,SNR and the number of energy levels. BER is the error rate when the receiver judge a single sample point and SER is the error rate that the receiver incorrectly decodes the symbol within a receiving window.
% For two energy levels, the BER and SER is p and pe. The r is SNR and m is the number of samples and it can on behalf of receiving length.
% For multiple energy levels, the BER and SER is pm and pem. The M is the number of energy levels.

## Slide 10
Temporal Modulation of WiZig
Preliminary Study
Design
Evaluation
(1) BER increases with the decrease of SNR
(2) BER increases with the increase of energy levels
(3) SER decreases with the increase of receiving window length
(1)
(2)
(3)
Notes: We can find that the BER will increase with the decreasing of SNR and it will increase when the
number of used energy levels increases.
The BER will be much higher when using more energy levels. The SER will decrease with the increasing length of receiving window.
In this case, we can adjust the length of receiving window to reduce error rate.

## Slide 11
Online Rate Adaptation
Preliminary Study
Design
Evaluation
Throughput Goal:
Notes: Based on the theoretical [,θiə'rɛtɪkəl] model, an online rate adaption algorithm is proposed to conquer the intrinsic channel Dynamics. It can adjust the number of energy levels and receiving window length adaptively according to current channel conditions.
The throughput object is Th. M is the number of energy levels, K is the length of receiving window. Pe is the SER and log2M represents the number of data bits that can be decoded within each receiving window.
If the new SNR is higher than the original, it means communication channel is getting better and there are three possible strategies to improve the throughput. First, we keep the window length unchanged and only increase the number of energy levels.
Second, we keep the number of energy level unchanged and only decrease the window length
Third, we both increase the number of energy level and decrease the window length at the same time.
Three different strategies can obtain three different throughput, then we can select the appropriate parameters of the number of energy level and window length to maximize the throughput.

## Slide 12
Evaluation
Evaluation Settings
One USRP acts as WiFi sender
Another USRP generates Gaussian noise
TelosB mote is used as ZigBee device
Preliminary Study
Design
Evaluation
Notes: We implement a prototype ['protə'taɪp] of WiZig.
one USRP acts as WiFi sender, another USRP generates Gaussian ['gaʊsiən] noise and TelosB mote is used as ZigBee device.

## Slide 13
SER and Throughput
Preliminary Study
Design
Evaluation
WiZig achieves higher throughput with lower SER
Notes: First, we study the performance of WiZig under varies noise intensities. We increase the channel noise.
We observe the variation of throughput and SER use the original setting with fixed parameters and online rate adaptation .
We can find that WiZig can achieve higher throughput with lower SER.

## Slide 14
Find out optimal parameters
Preliminary Study
Design
Evaluation
Our rate adaptation algorithm find the optimal parameters of energy levels and receiving window length (M, K) when the channel is noisy
noise=3dB
Noise=9dB
Noise=18dB
Notes: Due to our accurate ['ækjərət] channel models, our rate adaptation algorithm can always find the optimal ['ɑptəml] parameters of energy level and receiving window length (M, K) when channel
is noisy.
For example, When noise is 3dB, we can choose the energy level as 8 and window length as 1.1T to make the throughput maximization [ˌmæksɪmaɪ'zeʃn] and guaranteeing the SER requirements.

## Slide 15
Robustness of WiZig
Preliminary Study
Design
Evaluation
(1) SER increases corresponding to different modulation methods
(1)
(2) SER decreases with the increase of packet length
(2)
(3) SER is relatively small and stable when sample interval varies
(3)
Notes: Several other factors, for example, the modulation, the length of the sender packets and the sample rate of the receiver can also influence the SER.
If we use the fixed factors, we can find that SER will increase corresponding to different modulation methods SER will decrease with the increase of packet length
SER is relatively small and stable when sample interval varies.
It we use online rate adaptation, we can find that the performance of SER is stable and it is lower.

## Slide 16
WiZig vs. FreeBee
Preliminary Study
Design
Evaluation
The performance of WiZig is better than FreeBee
Notes: We also compare WiZig with FreeBee, a state-of-art cross-technology communication scheme.
When channel is clean, the performance of both FreeBee and WiZig are good. However, with the increase of noise, the SER of FreeBee will increase to be larger than the required threshold. the SER of WiZig will always be lower than 0.01.
In addition, The throughput of WiZig is always higher than FreeBee.

## Slide 17
Summary
Present a general framework of CTC, WiZig. It jointly employs amplitude and temporal modulation
Establish a theoretical model and propose an online rate adaptation algorithm to resist channel noise.
Evaluate the performance of WiZig using different experimental settings.
Preliminary Study
Design
Evaluation
Notes: In conclusion,
We present a general framework of CTC, which jointly employs modulation techniques in both the amplitude and temporal dimensions.
Based on this framework, we establish a theoretical model to clearly describe the relationship between BER (Bit Error Rate) and SNR (Signal to Noise Ratio). We also propose an online rate adaptation algorithm to optimize the throughput against dynamic noise.
We evaluate the performance of WiZig using different experimental settings. The results demonstrate that WiZig realizes efficient and reliable CTC under varied channel conditions.

## Slide 18
INFOCOM 2017
Q&A
Thanks
xiuzhenguo1994@gmail.com
Notes: Thank you so much for your attention, I’m happy to take your question.

## Slide 19
Backups

## Slide 20
Modulation/Demodulation Rules
Sender:
Presence/absence of packets: 1/0
Receiver:
(1)Detect the RSSI sequence
(2)A deciding thresholds the0 and number threshold thm
(3)For one sample: RSSI ≥ the0 , packet sample
(4)For each receiving window: the number of packet sample larger than thm, 1
Preliminary Study
Design
Evaluation
Notes: Suppose there are m packet samples (s1; s2; :::; sm) in a receiving window T. The demodulation rules are as follows.
(1) The WiZig sender transmits packets and encodes the
Presence of packets as bit”1” , the absence of packets as bit “0”.
(2)The receiver detects the RSSI sequences.
the receiver sets a deciding thresholds the0 and number threshold thm
(3)For each packet sample, its logic value will be decided as “1” if the sampling value RSSI ≥ the0. otherwise, it will be 0.
(4)For each receiving window, Decoded symbol will be “1” if the number of packet sample larger than thm.
According to the majority vote, the threshold thm is half of the total number of sample points.

## Slide 21
Theoretical Analysis
Assuming the channel is an additive white Gaussian noise channel (AWGN)
Noise:
Signal:
For one sample
(1)
Preliminary Study
Design
Evaluation
Notes: First, we build a model that describes the relationship between BER and SNR for one sample.
Assuming the channel is an additive white Gaussian noise channel (AWGN), with the mean of 0 and the variance of 2n , Its one-dimensional probability density is
Suppose the transmission power of WiZig sender is a. Then the signal at the receiver is the superposition of sending signal and channel noise. Its one-dimensional probability density is
Denote the probability that sender sends 1 and 0 as P(1) and P(0). the total error rate of receiver p can be calculated as follows.

## Slide 22
Theoretical Analysis
For one sample, If we denote the decoding threshold as b, the decision rule
is as follows:
(1) x > b, the point is decoded as 1.
(2) x ≤ b, the point is decoded as 0.
(2)
(3)
Preliminary Study
Design
Evaluation
Notes: The probabilities that the receiver decode 1/0 incorrectly as 0/1 are P(0|1) and P(1|0), respectively.
where P(0|1) is the probability the receiver decode 1 as 0 and P(1|0) is the probability the receiver decode 0 as 1.

## Slide 23
Theoretical Analysis
p is related with decision threshold b and signal strength a
For one receiving window:
If M energy levels are used
(4)
(5)
(6)
(7)
Preliminary Study
Design
Evaluation
Notes: we can find that p is related with decision threshold b and signal strength a. We can obtain the optimal decision threshold b∗ = a/2 to minimize the total error rate p by
letting @p/@b = 0.
When we choose b∗ = a/2 , p can be calculated as follows and shown in the shaded area
This is the relationship between BER and SNR for one RSSI sample
Assuming the receiver gets m samples in a receiving window, if the number of samples that are decided as 1 by the receiver and the sender also transmits the same is less
than a threshold, the receiver can decode symbol correctly within a receiving window.
If M energy levels are used, BER and SER can be represented as pm and pem respectively.

## Slide 24
Maximum energy level:
Maximum energy level
Preliminary Study
Design
Evaluation
Notes: How many energylevels can be divided at most in theory?
To answer this question, we first investigate how large does the RSSI gap between two adjacent energy levels can be.
We control the SNR as 7 dB and the RSSI gap between packets and noise is large.
Second, we control the SNR as 1 dB and the RRSI gap between packets and noise is too small to judge the packets . This will result in high SER.
Third, the snr is 4 dB. The RSSI gap is enough to separate packets from noise and not too large to waste the coding space. The proper RSSI gap to separate
two energy levels is decided by SNR. Given a required BER, a minimum RSSI gap △RSSI can be calculated to provide appropriate SNR.
RSSI is the max signal strength at the receiver and △RSSI is the minimum RSSI gap between two adjacent energy levels.
We control one AP
as transmitter and three other APs as noise sources to observe
the effectiveness of energy coding under different RSSI gaps.

## Slide 25
Temporal Modulation of WiZig
Preliminary Study
Design
Evaluation
Notes: The relationship between BER and SNR is
We can find that different SNR threshold is required to satisfy different BER. For example,
for the BER of 0.01, SNR needs to be 10 dB. But for the BER of 0.1, SNR only needs 3 dB. So for some system BER requirements, it is only needs SNR to be larger than a certain threshold and strictly high SNR is not necessary.
Compared with Amplitude modulation, Temporal modulation is relatively more robust to noise. We propose temporal modulation to be more resilient to the dynamic noise on wireless channel.

## Slide 26
11
26
2405MHz
2MHz
5MHz
WiFi
ZigBee
RSSI
CSI
Reverse Link: From ZigBee to WiFi
Preliminary Study
Design
Evaluation
Notes: WiZig can be used for the bi-directional communication between WiFi and ZigBee.
But it is usually not easy to accomplish high data rate from ZigBee to WiFi due to the low transmission power of ZigBee.
Besides, the asymmetric [,esɪ'mɛtrɪk] channel widths [wɪdθ] of ZigBee and WiFi also needs to be considered. A typical WiFi channel is usually 20MHz['mɛɡəhɝts], which is
much wider than a ZigBee channel. The OFDM modulation of WiFi divides the
20MHz band into several subcarriers (e.g., 64 subcarriers in IEEE 802.11 a/g/n/ac). As a result, a ZigBee transmission can
affect several WiFi subcarriers.
Hence, from ZigBee to WiFi, instead of RSSI, Channel State Information (CSI) may be more
suitable to capture the energy levels on each subcarrier. Then the CSI can be used to extract the overlapping subcarriers of the ZigBee transmission

## Slide 27
Overhead of WiZig
Applications | Duty cycle (%)
Surfing new sites | 89.37
Audio | 92.84
YouTube Video 360p | 93.29
YouTube Video 1080p | 93.45
File Transfer | 66.40
Skype voice | 11.05
Skype video | 15.65
The extra packets overhead of WiZig
is affordable to achieve the high-rate CTC communication.
W. Joseph, D. Pareit, D. Naudts, G. Vermeeren, I. Moerman, and L. Martens, “Duty cycles of wireless applications and activities for wifi exposure assessment,” in Joint Meeting of the Bioelectromagnetics Society and the European BioElectromagnetics Association, pp. 63–65, 2013.
Preliminary Study
Design
Evaluation
Notes: Another question worth discussion is the impact of WiFi traffic on the WiZig communication.
The transmission of WiZig is an on-demand mode. WiZig leverages the absence and presence of WiFi packets to transmit CTC messages. Hence, the off-the-shelf traffic can be used. But the amount of traffic affects how many additional packets we need to inject.
In most practical indoor scenarios, when there are multiple active WiFi devices, the duty cycle of WiFi traffic is enough to use.
In some circumstances, the duty cycle of applications is lower than the required. Whereas, the extra packets overhead of WiZig is affordable to achieve the high-rate CTC communication.

## Slide 28
How to use the WiZig for the applications in upper layers
CSMA RTS/CTS
Pre-defined preamble
payload
Detect RSSI
Switch to CTC mode
Preliminary Study
Design
Evaluation
Notes: As a communication framework, WiZig is easy to use for the applications in upper layers. three steps are needed
First, the WiFi sender leverages the method of Carrier Sense Multiple
Access (CSMA) to preempt [prɪ'empt] clear channel and avoid the interference
of other homogeneous [,homə'dʒinɪəs] devices. In addition, RTS/CTS
can also be used to avoid hidden terminal problem.
Second,
a pre-defined preamble ['priæmbl] is transmitted by the sender ahead of
the data frames. When the ZigBee
receiver detects signals, it first decodes packets followed the
standard of IEEE 802.15.4. If the decoding fails, the receiver
analyzes the detected RSSI sequences to see whether the signal
comes from WiFi or not [11]. If the on-going signal is from
WiFi, the ZigBee receiver switches to CTC mode and decodes
the messages according the demodulation of WiZig.