## Slide 1: ZigFi: Harnessing Channel State Information for Cross-Technology Communication

## Slide 2
CTC from ZigBee to WiFi
Physical Level Emulation
 | ZigBee | WiFi
Center Frequency | 2405+5(k-11) | 2412+5(k-1)
Modulation | DSSS | OFDM
Encoding | OQPSK | BPSK\QPSK\QAM
Rate | 250 Kbps | 54 Mbps
 | Simple | Complex
It is difficult to emulate WiFi for ZigBee

## Slide 3
Asymmetric transmission power of ZigBee vs. WiFi
Physical Level Emulation
CTC from ZigBee to WiFi
Infeasibility of ZigBee to WiFi CTC using RSSI

## Slide 4
Asymmetric bandwidth of ZigBee vs. WiFi
Physical Level Emulation
CTC from ZigBee to WiFi
Feasibility of ZigBee to WiFi CTC using CSI

## Slide 5
CSI sequence on different subchannels
The transmission of ZigBee packets affects the CSI sequence of the WiFi receiver
The variation of the CSI sequence at each subcarrier is different

## Slide 6
CSI sequences with different ZigBee packet lengths
One ZigBee packet overlaps with at least one WiFi packet

## Slide 7
CSI sequences with different ZigBee transmit power
If the ZigBee power is low, the CSI variation will be too little to be detected at the WiFi receiver.
If the ZigBee power is too high, the WiFi preamble will be subjected to strong interference impacting regular WiFi traffic

## Slide 8
On classifying CSI sequences: SVM
There are no simple rules to describe the variation of CSI values
The two sets of CSI pair overlap with each other
Use a classifier and map the CSI features to higher dimensional space

## Slide 9
ZigFi Design

## Slide 10
Decoding with a CSI classifier
the performance of SVM is related with the window length (CSI samples)
Choose the window length is 8

## Slide 11
The relationship between the Accuracy and the SINR
A new metric SINR in ZigFi
SINR in range [-0.25,1.25], decoding accuracy > 0.9

## Slide 12
The Receiver-initiated mechanism
Establish a WiFi Link
Adaptively adjust ZigBee and WiFi power to obtain
an appropriate SINR

## Slide 13
Evaluation
Implementation
Comparison ZigFi vs. FreeBee

## Slide 14
Evaluation
ZigFi under different distance between the ZigBee sender and the WiFi sender
ZigFi performance under different distance between the WiFi sender and the WiFi receiver

## Slide 15
Evaluation
ZigFi performance under different intensity of noise
ZigFi performance under different distance between the ZigBee sender and the WiFi receiver in the NLOS scenario

## Slide 16
Evaluation
The SER and throughput of multiple-to-one concurrent transmissions

## Slide 17
Thank
Q&A